## Slide 1: Module 4: Oxygen therapy

## Slide 2
Objectives
Indications of oxygen therapy
Detection of hypoxaemia
Oxygen delivery methods
Monitoring of oxygen therapy
Complications of hypoxia and hyperoxia

## Slide 3: Conditions associated with hypoxaemia
Neonates
  Respiratory Distress Syndrome
  Neonatal pneumonia
  Transient tachypnoea of newborn
Children
  Pneumonia
  Interstitial lung disease
  Severe asthma
  Pulmonary edema
Neonates
  Severe Birth asphyxia
  Sepsis
  Congenital heart defects
Children
  Shock
  Meningitis
  Perioperative emergencies
  Trauma
  Carbon monoxide poisoning
WHO Oxygen therapy for children 2016

## Slide 4: How to detect hypoxaemia
Computerized unit and a sensor probe, which is attached to the patient
Displays the SpO2 with an audible signal for each pulse beat and the pulse rate
Hypoxaemia is SpO2<90%
Measures the partial pressure of oxygen (PaO2)and carbon dioxide in blood
Also measures blood pH and the concentrations of the main electrolytes
Hypoxaemia is PaO2< 60mmHg
It is important for health workers to be able to identify clinical signs of hypoxaemia
Combination of clinical signs increases the chances of detecting hypoxaemia
WHO 2016: Oxygen therapy for children: a manual for health workers
Clinical Signs
Pulse Oximetry
Blood Gas Analysis
Notes: If oximetry is not available, the following clinical signs could be used to determine use of oxygen therapy:
• central cyanosis
• nasal flaring
• inability to drink or feed (when due to respiratory distress)
• grunting with every breath
• depressed mental state (i.e. drowsy, lethargic)
In some situations, and depending on the overall clinical condition, children with the following less specific signs may also need oxygen:
• severe lower chest wall indrawing
• respiratory rate ≥ 70/min
• head nodding

## Slide 5: Pulse oximetry in detection of hypoxaemia
Clinical use
Advantages
Most accurate non­invasive method for detecting hypoxaemia
Measures the percentage of oxygenated haemoglobin in arterial blood (SpO2)
Performed on all patients requiring admission
In the outpatient department for children with fast RR & LCWI.
Reliable monitor for hypoxaemia- 5th Vital sign
Detects 20–30% more children with hypoxaemia than clinical signs alone
Non –invasive and painless unlike blood gas analysis
Easy to use
Inexpensive and widely available
All health facilities should have a pulse oximeter with a neonatal & paediatric probe!
WHO 2016: Oxygen therapy for children: a manual for health workers
What it measures
Notes: pulse oximetry measures oxygen saturation by illuminating the skin and measuring changes in light absorption of oxygenated (oxyhemoglobin) and deoxygenated blood (reduced hemoglobin) using two light wavelengths: 660 nm (red) and 940 nm (infrared) .

## Slide 6: Using the Pulse Oximeter
Attach probe to pulse oximeter
Press the power button to turn on the pulse oximeter
Ensure the probe has a red light and the settings are appropriate
Choose a well perfused site to attach probe
Attach the probe making sure the light source and sensor line up
Allow a normal trace to establish
Read the oxygen saturation
a)
b)
c)
d)
e)

## Slide 7: Oxygen Delivery Methods
Kenyan Pediatric protocol 2016; WHO oxygen therapy for children 2016 : https://www.who.int/maternal_child_adolescent/documents/child-oxygen-therapy/en/
Non-Rebreather Mask)
Nasal Prongs
bCPAP
Nasal Catheter

## Slide 8: Titrating & Stopping Oxygen (Refer to BPP 2022 Page 28)
When Oxygen is started, titrate every 15-30mins by 0.5L/min until SpO2 is 90-96%
Change the oxygen delivery methods (nasal prongs, catheter or NRM) and flow rates based on need
Stop titrating and begin close monitoring if clinically stable (no emergency signs, SpO2 > 90% and no increase WoB)
Wean off oxygen every 15 –30 min and carefully examine for changes in WoB and SpO2 to assess whether supplemental oxygen is still required.
Once oxygen is stopped, recheck SpO2 after 1h, as late desaturation can sometimes occur.
Discharge only if child has been stable with SpO2 ≥ 90% and no increased WoB on room air for at least 24hrs
WHO oxygen therapy for children 2016 : Sources and delivery of oxygen; page 32-33

## Slide 9: Complications of oxygen therapy a) O2 toxicity (Hyperoxia, overdose >96%)
Makes them constrict which reduces blood supply to the organs
Can cause chest pain and irritation of the airway.
In the term long term can cause lung stiffness (fibrosis)
Respiratory system
CNS
Peripheral vessels
Helmerhorst, H.J.F., Schultz, M.J., van der Voort, P.H.J. et al. Bench-to-bedside review: the effects of hyperoxia during critical illness. Crit Care 19, 284 (2015). https://doi.org/10.1186/s13054-015-0996-4
Produces toxic substances that destroys nerves making a patient present with symptoms e.g. convulsions

## Slide 10
Respiratory system
Makes the vessels in the lungs constrict and if they constrict for long this can cause high pressure in the lungs (pulmonary hypertension)
Makes all cells in the body function abnormally leading to organ failure and death
All body organs
Michiels C. (2004). Physiological and pathological responses to hypoxia. The American journal of pathology, 164(6), 1875–1882. https://doi.org/10.1016/S0002-9440(10)63747-9
Complications of oxygen therapy b) Hypoxia (underdose <90%)

## Slide 11: Summary
O₂
  Use of clinical signs should be augmented by use of objective measures e.g. by use of pulse oximeters
  Oxygen is a medicine, therefore it should be measured, given at the right dose and only when indicated.
  Correctly identify and administer oxygen to patients who need oxygen